## Slide 1
6.0 Time/Frequency Characterization
of Signals/Systems
      6.1 Magnitude and Phase for Signals
      and Systems

## Slide 2
Signals
  : magnitude of each frequency component
  : phase of each frequency component

## Slide 3
  Time Shift
(P.23 of 4.0)

## Slide 4
  Sinusoidals (p.25 of 4.0)

## Slide 5
Signals
Example
      See Fig. 3.4, p.188 and Fig. 6.1, p.425 of text
  change in phase leads to change in time-domain characteristics
  human auditory system is relatively insensitive to phase of sound signals

## Slide 8
Signals
Example : pictures as 2-dim signals
  most important visual information in edges and regions of high contrast
  regions of max/min intensity are where different frequency components are in phase
      See Fig. 6.2, p.426~427 of text

## Slide 9
Two-dim Fourier Transform
fixed
different

## Slide 10
    Problem 3.70, p.281 of text
2-dimensional signals
(P.65 of 3.0)

## Slide 13
Systems
  : scaling of different frequency components
  : phase shift of different frequency
  components

## Slide 14
Systems
Linear Phase (phase shift linear in frequency) means
constant delay for all frequency components
  slope of the phase function in frequency is the delay
  a nonlinear phase may be decomposed into a linear part plus a nonlinear part

## Slide 15
  Linear Phase for Time Delay
1
Scope=
Delay

## Slide 16
Time Shift
phase shift linear in frequency with amplitude unchanged
(P.28 of 3.0)
Time Shift
  linear phase shift (linear in frequency) with amplitude unchanged

## Slide 17
  Time Shift
(P.23 of 4.0)

## Slide 18
Systems
Group Delay at frequency ω
  common delay for frequencies near ω

## Slide 19
Systems
Examples
  See Fig. 6.5, p.434 of text
  Dispersion : different frequency components delayed
  by different intervals
  later parts of the impulse response oscillates at near 50Hz
  Group delay/magnitude function for Bell System telephone lines
      See Fig. 6.6, p.435 of text

## Slide 22
Systems
Bode Plots
  ω not in log scale, finite within [ -,  ]
Discrete-time Case
Condition for Distortionless
  Constant magnitude plus linear phase in signal band

## Slide 23
  Distortionless
Signal
band

## Slide 24
      6.2 Filtering
Ideal Filters
Low pass Filters as an example
  Continuous-time or Discrete-time
  See Figs. 6.10, 6.12, pp.440,442 of text
  mainlobe, sidelobe, mainlobe width

## Slide 25
1
0
1
1
0
0
  Filtering of Signals
  (p.59 of 4.0)

## Slide 28
Ideal Filters
Low pass Filters as an example
  with a linear phase or constant delay
  See Figs. 6.11, 6.13, pp.441,442 of text
  causality issue
  implementation issues

## Slide 31
  Realizable Lowpass Filter
0
0
0
  (p.62 of 4.0)

## Slide 32
Ideal Filters
Low pass Filters as an example
  step response
      See Fig. 6.14, p.443 of text
      overshoot, oscillatory behavior, rise time

## Slide 34
Nonideal Filters
Frequency Domain Specification
(Lowpass as an example)
  δ1(passband ripple), δ2(stopband ripple)
  ωp(passband edge), ωs(stopband edge)
  ωs - ωp(transition band)
  phase characteristics
magnitude
characteristics
      See Fig. 6.16, p.445 of text

## Slide 35
  δ1(passband ripple), δ2(stopband ripple)
  ωp(passband edge), ωs(stopband edge)
  ωs - ωp(transition band)
magnitude
characteristics

## Slide 36
Nonideal Filters
Time Domain Behavior : step response
  tr(rise time), δ(ripple), ∆(overshoot)
  ωr(ringing frequency), ts(settling time)
      See Fig. 6.17, p.446 of text

## Slide 37
  tr(rise time), δ(ripple), ∆(overshoot)
  ωr(ringing frequency), ts(settling time)

## Slide 38
Nonideal Filters
Example: tradeoff between transition band width
(frequency domain) and settling time (time domain)
      See Fig. 6.18, p.447 of text

## Slide 40
Nonideal Filters
Examples
  linear phase
  See Figs. 6.35, 6.36, pp.478,479 of text
  A narrower passband requires longer impulse response

## Slide 43
Nonideal Filters
Examples
  A more general form
  See Figs. 6.37, 6.38, p.480,481 of text
  A truncated impulse response for ideal lowpass filter gives much sharper transition
  See Figs. 6.39, p.482 of text
  very sharp transition is possible

## Slide 47
Nonideal Filters
To make a FIR filter causal

## Slide 48
      6.3 First/Second-Order Systems
      Described by Differential/Difference
      Equations
Continuous-time Systems by Differential Equations
  Higher-order systems can usually be represented as combinations of 1st/2nd-order systems
  first-order
  second-order
        See Fig. 6.21, p.451 of text

## Slide 50
Discrete-time Systems by Differential Equations
  first-order
  second-order
        See Fig. 6.26, 27, 28, p.462, 463, 464, 465 of text

## Slide 51
First-order Discrete-time system (P.461 of text)
x[n]
y[n]
D
a
y[n-1]

## Slide 57
…
    Examples
  (p.114 of 2.0)

## Slide 58
Second-order Discrete-time system (P.465 of text)
,

## Slide 59
    Problem 5.46, p.415 of text
F
F
F
F
  (p.85 of 5.0)

## Slide 60
    Problem 6.59, p.508 of text
0

## Slide 61
All truncated dimensions are orthogonal to the subspace of dimensions kept.
  Truncated Dimensions
, ,
for orthogonal , ,
  (p.21 of 3.0)

## Slide 62
.
.
.
    Problem 3.66, p.275 of text
  (p.62 of 3.0)

## Slide 63
    Problem 6.64, p.511 of text
(a)
(b)
(c)
(4.3.3 of Table 4.1)
0
0
0