## Slide 1: Circuits Lecture 2: Node Analysis
李宏毅 Hung-yi Lee

## Slide 2: DC Circuit - Chapter 1 to 4
KCL, KVL, Element Characteristics
Node Analysis
Mesh Analysis
Controlled Sources
Equivalent
Thevenin Theorem
Norton Theorem
Lecture 1
Lecture 2
Lecture 3
Lecture 4
Lecture 5&6
Lecture 7
Lecture 8
Lecture 9
Superposition
Notes: Not follow the order
Slow
Detailed slide
Practice examples

## Slide 3: Review – Lecture 1
A
B
+
-
If v<0, then actually ……
If i<0, then actually ……
A
B
A
B
+
-
Resistor with resistance R:
reference current should flow from “+” to “-”

## Slide 4: Review – Lecture 1
Voltage defined for two points
Potential defined for one point
  Voltage between the point and the reference
A
B
+
-
A
B
+
-

## Slide 5: Review – Lecture 1
KCL:
KVL
Loop 1:
Loop 1

## Slide 6: Review – Lecture 1
Find the current and voltage of all elements.
Systematic Solution:
Step 1. List all unknown variables and reference directions
Step 2. Use (a) Element Characteristics, (b) KCL and (c) KVL to list equations for unknown variables
How to reduce the number of unknown variables?

## Slide 7: Textbook
Chapter 4.1

## Slide 8: Terminology
Node: any connection point of two or more circuit elements (Textbook, P23)
  Essential node: more than two elements
  Non-essential node: two elements
  Use “node” to represent “Essential node”
Branch:
  Circuit between nodes

## Slide 9: Node Analysis
Current + Voltage
Voltage
Only consider the voltage as unknown variables
Reduce the number of unknown variables
Usually it is easy to find current if the voltages are known
A
B
+
-
Resistor with resistance R
How about ……
i??????

## Slide 10: Node Analysis
Current + Voltage
Voltage
Voltages are not independent
If we know the voltage of some elements, we can know the rest easily (KVL)
Maybe we only have to consider some of the voltages as unknown variables
How to determine the voltage taken as unknown variables?
+
-
-
+
+
-
+
-
v1
v2
v3
v4 = v1 + v2 – v3
Notes: Why hard to determine?

## Slide 11: Node Analysis
Current + Voltage
Voltage
Node Potential
(Node Voltage)
The potentials are independent
10V
15V
Target: node potential
A
B
+
-
Can know voltage immediately
Any potential value can satisfy KVL
+
-
-
+
+
-
+
-

## Slide 12: Node Analysis
Find node potentials
  3 unknown variables
KVL:
+
-
+
-
+
-
Represent vb, vc and vd by node potentials
KVL is automatically fulfilled!

## Slide 13: Node Analysis
Find node potentials
  3 unknown variables
KCL:
Represent ia, ib and ic by node potentials
Can we always represent current by node potentials (discuss later)?
Node v1:

## Slide 14: Node Analysis
Find node potentials
  Need 3 equations
KCL:
Node v1:
Node v2:
Node v3:

## Slide 15: Node Analysis
Target: Find node potentials
Steps
  1. Set a node as reference point
  2. Find nodes with unknown node potentials
  3. KCL for these nodes
    Input currents = output currents
    Represent unknown current by node potentials
      Always possible?

## Slide 16: 8 Kinds of Branches
There are only 8 kind of branches
  1. None
  2. Resistor
  3. Current
  4. Current + Resistor
  5. Voltage
  6. Voltage + Resistor
  7. Voltage + Current
  8. Current + Resistor + Voltage
Represent i by node potentials
branch

## Slide 17: Branch: Voltage + Resistor

## Slide 18: Branch: Voltage + Resistor - Example
Find vo

## Slide 19: Branch: Voltage
Method 1:
Beside node potential, consider i also as unknown variable as well
Represent i1 to i6 by
node potential
One more unknown variable i, need one more equation

## Slide 20: Branch: Voltage
Method 2:
Consider vx and xy as supernode
Represent i1 to i6 by node potential
Bypass i

## Slide 21: Branch: None
Supernode

## Slide 22: Example 4.5
Use node analysis to analyze the following circuit

## Slide 23: Example 4.5
Use node analysis to analyze the following circuit

## Slide 24: Example 4.5
KCL for Supernode:
KCL for v2:

## Slide 25: Node Analysis – Connected Voltage Sources

## Slide 26: Node Analysis – Connected Voltage Sources
If a branch starts and ends at the same super node
Put it into the supernode

## Slide 27: Node Analysis – Reference Points
We don’t have to draw supernode.
Select the reference point carefully

## Slide 28: Homework
4.18
4.22

## Slide 29: Thank you!

## Slide 30: Answer
4.18
  V1=-6, v2=12, i1=2, i2=3, i3=2.4
4.22
  V1=-16.5, v2=30, i1=2, i2=0.5

## Slide 31: Branch: Voltage – Special Case!
If vy is selected as reference
vx is equal to vs
The node potential is known
Eliminate one unknown variables
    Which node should be selected as reference point?
Ans: The node connected with voltage source