## Slide 1: Circuits Lecture 4: Superposition
李宏毅 Hung-yi Lee

## Slide 2: Outline
Matrix Equation for Node and Mesh analysis
  Chapter 4.1, 4.2
Superposition
  Chapter 2.4

## Slide 3: Node Analysis
v1:
v2:
v3:

## Slide 4: Node Analysis
You can directly write the matrix equation below.
Resistance
Node potentials
Sources
(textbook, P139)

## Slide 5: Node Analysis
v1, v2, v3 is the weighted sum of is and vs
Node potential is the weighted sum of the values of sources
Voltage (potential difference) is the weighted sum of the values of sources
Notes: Invertible? yes
Levy-Desplanques theorem asserts that a strictly diagonally dominant matrix is invertible
https://www.youtube.com/watch?v=TDWKLAAWbkY

## Slide 6: Mesh Analysis
For mesh 1
Ra(i1-is)+Rbi1+Rc(i1-i2)-vs=0
For mesh 2
Rc(i2-i1)+Rdi2+Re(i2-i3)=0
For mesh 3
Re(i3-i2)+Rfi3+vs=0
You can directly write the matrix equation below.
(textbook, P153)

## Slide 7: Mesh Analysis
Resistance
Mesh Current
Sources

## Slide 8: Mesh Analysis
i1, i2, i3 is the weighted sum of is and vs
Mesh currents are the weighted sum of the values of sources
Currents of the braches are the weighted sum of the values of sources

## Slide 9: Linearity
  y: any current or voltage for an element
  xi: current of current sources or voltage of voltage sources
Any current (or voltage) for an element is the weighted sum of the voltage (or current) of the sources.
Based on node and mesh analysis:
Notes: Not for dynamic circuit

## Slide 10: Linearity - Example
Any current (or voltage) for an element is the weighted sum of the voltage (or current) of the sources.

## Slide 11: Not apply on Power
  xi: current of independent current sources or voltage of independent voltage sources
Voltage:
Current:
Power:
Power:

## Slide 12: Proportionality Principle – One Independent Sources
Find i1 and v1 when vs is 9V, 72V and 0.9V
Complex
Circuit

## Slide 13: Superposition Principle – Multiple Independent Sources
Example 2.10
  Find i1
We can find i1-1, i1-2, i1-3 separately.
When x2=0 and x3=0,
The current through 2Ω is i1-1.

## Slide 14: Superposition Principle – Multiple Independent Sources
Example 2.10
  Find i1
We can find i1-1, i1-2, i1-3 separately.
Current of current source set to be zero.
Open Circuit

## Slide 15: Superposition Principle – Multiple Independent Sources
Example 2.10
  Find i1
We can find i1-1, i1-2, i1-3 separately.
To find i1-2, we set x1=0 and x3=0.
Now the current through 2Ω is i1-2.

## Slide 16: Superposition Principle – Multiple Independent Sources
Example 2.10
  Find i1
We can find i1-1, i1-2, i1-3 separately.
Voltage of voltage source set to be zero.
Short Circuit

## Slide 17: Superposition Principle – Multiple Independent Sources
Example 2.10
  Find i1
We can find i1-1, i1-2, i1-3 separately.

## Slide 18: Superposition Principle – Multiple Independent Sources
Example 2.10
  Find i1
We can find i1-1, i1-2, i1-3 separately.
set x2=0 and x3=0
set x1=0 and x3=0
set x1=0 and x2=0

## Slide 19: Superposition Principle – Multiple Independent Sources
  Steps to apply Superposition Principle:
    If the circuit has multiple sources, to find a voltage or current for an element
    For each source
      Keep the source unchanged
      All the other sources set to zero
        Voltage source’s voltage set to 0 = Short circuit
        Current source’s current set to 0 = open circuit
      Find the voltage or current for the element
    Add all the voltages or currents obtain by individual sources

## Slide 20: Remind
Always using superposition when there are multiple sources?
One circuit (3 sources)
v.s.
Three circuits (1 source)

## Slide 21: Concluding Remarks
This equation only for circuits with sources and resistors.
  y: any current or voltage for an element
  xi: current of current sources or voltage of voltage sources
Proportionality Principle, Superposition Principle
Can be used in any circuit in this course

## Slide 22: Linearity
A circuit is a multiple-input multiple-output (MIMO) system
  Input: current of current sources or voltage of voltage sources
  Output: the current or voltage for the elements
+
-
Circuit
(System)
input
output

## Slide 23: Linearity
All linear circuits are linear system
Linear Circuit:
  Sources
  Linear Elements:
    Resistor, Capacitor, Inductor
  All circuits in this courses are linear circuits.
  All circuits in this courses are linear systems.

## Slide 24: Linearity
Linear System:
  Property 1:
  Input: g1(t), g2(t), g3(t), ……
  output: h1(t), h2(t), h3(t), ……
  Input: Kg1(t), Kg2(t), Kg3(t), ……
  output: Kh1(t), Kh2(t), Kh3(t), ……
Proportionality Principle

## Slide 25: Linearity
Linear System:
  Property 2:
  Input: a1(t), a2(t), a3(t), ……
  output: x1(t), x2(t), x3(t), ……
  Input: a1(t)+ b1(t), a2(t)+ b2(t), a3(t)+ b3(t), ……
  output: x1(t)+y1(t), x2(t)+y2(t), x3(t)+y3(t), ……
Superposition Principle
  Input: b1(t), b2(t), b3(t), ……
  output: y1(t), y2(t), y3(t), ……

## Slide 26: Linearity
Linear System:
  Property 2:
  Input: a1(t), a2(t), a3(t), ……
  output: x1(t), x2(t), x3(t), ……
  Input: a1(t)+ b1(t), a2(t)+ b2(t), a3(t)+ b3(t), ……
  output: x1(t)+y1(t), x2(t)+y2(t), x3(t)+y3(t), ……
Superposition Principle
  Input: b1(t), b2(t), b3(t), ……
  output: y1(t), y2(t), y3(t), ……

## Slide 27: Linearity
Superposition Principle can be applied on any circuit in this course (Textbook: Chapter 6.5).

## Slide 28: Homework
2.50
Given vs and R3, find vb

## Slide 29: Homework
2.52
Given is, find vs such that v4= 36V

## Slide 30: Thank you!

## Slide 31: Answer
2.50
  -12V
2.52
  60V