## Slide 1: Circuits Lecture 8: Thevenin and Norton Theorem (1)
李宏毅 Hung-yi Lee

## Slide 2: Textbook
Chapter 2.5

## Slide 3: Network
A two-terminal network is a function represented by i-v characteristics
Given a network, computing its i-v characteristics, and then label it with simpler equivalent network
v
i

## Slide 4: Computing i-v characteristics
i
v
Add a voltage source v
Find i
v is a unknown variable
Represented by v
Obtain the relation of i and v
Add a current source i
Find v
i is a unknown variable
Represented by i
Obtain the relation of i and v
v
i

## Slide 5: Computing i-v characteristics
i
v
Voltage source v
Independent Sources
x1, x2, x3 ……
i is the weighted sum of the voltage (or current) of the sources.
The relation of i and v is linear!
constant

## Slide 6: Computing i-v characteristics
The v-i characteristics is linear!
v
i
Case 1: current source
Case 2: voltage source
Case 3: resistor
i=mv
  Resistor
  with resistance 1/m Ω
  m>0, normal resistor
  m<0, ?
  Negative resistor

## Slide 7: Computing i-v characteristics
v
i
Case 4: resistor +voltage source
Notes: How about other direction?

## Slide 8: Computing i-v characteristics
The v-i characteristics is linear!
v
i
Case 1: current source
Case 2: voltage source
Case 3: resistor
Case 4: resistor +voltage source

## Slide 9: Thevenin Theorem
Two
Terminal
Network
    Two terminal network consists entirely of independent source, resistor and controlled sources.
    If controlled sources are present, then the control variables is within the same network.
Find voc and Rt directly without drawing i-v characteristics?
Notes: Two versions of Thevenin :
weak vs strong
Why for the controlled sources?

## Slide 10: Thevenin Theorem - voc
Two
Terminal
Network
Keep two terminals open

## Slide 11: Thevenin Theorem - Rt
(As we have done in Superposition)
Textbook P72 - 73
Voltage Source
Suppress the independent sources:
Current Source
Short
Open
Why?????

## Slide 12: Thevenin Theorem - Rt (Example)
Refer to lecture 7
Suppress the independent sources

## Slide 13: Thevenin Theorem - Rt
Superposition:
v
Independent Sources in network: x1, x2, x3 ……
i
Voltage source v

## Slide 14: Norton Theorem
Two
Terminal
Network
Thevenin
Theorem
Norton
Theorem

## Slide 15: Norton Theorem - isc
Two
Terminal
Network
Let two terminals short
If we already know voc, Rt=voc/isc
After we find isc,
If we already know Rt, voc=iscRt

## Slide 16: Thevenin Parameters
Voc, Rt and isc are Thevenin parameters
  voc: keep the two terminals open
  Rt: suppress the independent sources
  isc: let the two terminals short
Know any of two can find the last one
Notes: Real application

## Slide 17: Example 2.14

## Slide 18: Example 2.14
Open circuit
Short Circuit
Set to Zero
Find voc
Find isc
Find Rt

## Slide 19: Example 2.14
Short Circuit
Then “open circuit” or “source set to zero”?

## Slide 20: Example 2.14
Source set to zero
Find equivalent resistance Rt

## Slide 21: Example 2.14

## Slide 22: Example 2.14
Check: Open circuit

## Slide 23: Example
Find the current and voltage on RL
Three-terminal networks?
Thevenin Theorem
Circuit Analysis
Obliterate RL

## Slide 24: Example
Find the current and voltage on RL
Find Thevenin Parameters
+
-
i

## Slide 25: Example
Find the current and voltage on RL
Open circuit
Short Circuit
Set to Zero
Find voc
Find isc
Find Rt

## Slide 26: Example
Find the current and voltage on RL
Open circuit
Find voc
So easy!

## Slide 27: Example
Find the current and voltage on RL
Short Circuit
Find isc
R1, R2, R3, R4:
(last page)

## Slide 28: Example
Find the current and voltage on RL
Set to Zero
Find Rt
Simple (but hard to figure out)
Check by yourself
Notes: Draw the process on the black broad

## Slide 29: Example
Find the current and voltage on RL
+
-
i

## Slide 30: Homework
2.62, 2.64

## Slide 31: Homework

## Slide 32: Homework

## Slide 33: Thank you!

## Slide 34: Answer
2.62
  Rt=5k, isc=vs/8k, voc=5vs/8
2.64
  Rt=-60, isc=is, voc=-60is

## Slide 35: Homework
Rt=100k,isc=-20m

## Slide 36: Homework
Rt=-1k/60, voc=2

## Slide 37: Acknowledgement
  感謝 徐瑞陽(b02)
  糾正錯誤的作業答案
  感謝 林楷恩(b02)
  糾正錯誤的作業答案