## Slide 1: Lecture 6 Controlled Sources (2)
Hung-yi Lee

## Slide 2: Outline
Node analysis with Controlled sources
  Chapter 4.3
Mesh analysis with Controlled sources
  Chapter 4.3
Superposition with Controlled sources
  Chapter 2.4

## Slide 3: Outline
Node analysis with Controlled sources
  Chapter 4.3
Mesh analysis with Controlled sources
  Chapter 4.3
Superposition with Controlled sources
  Chapter 2.4

## Slide 4: Node Analysis - Review
Target: Find node potentials
Steps:
  1. Set a node as reference point
  2. Find nodes with unknown node potentials
  3. KCL for these nodes
    Represent unknown current by node potentials

## Slide 5: Node Analysis with Controlled Sources
Consider the controlled sources just as independent sources
  But with current or voltage as unknown variables
List the equations with node potentials and current or voltage of controlled sources
Represent current or voltage of the controlled sources by node potentials
  Can you we that?
Obtain equations only with node potentials

## Slide 6: Node Analysis with Controlled Sources
Voltage controlled
Easy to represent control variable vx by node potentials

## Slide 7: Node Analysis with Controlled Sources
Current controlled
In most cases, we can represent the control variable ix by node potentials (refer to slides of Lecture 2)
Except that when ix is the current of voltage sources

## Slide 8: Problem 4.58 – CCCS, VCVS
Node 1:
Node 2:

## Slide 9: Outline
Node analysis with Controlled sources
  Chapter 4.3
Mesh analysis with Controlled sources
  Chapter 4.3
Superposition with Controlled sources
  Chapter 2.4

## Slide 10: Mesh Analysis - Review
Target: Find mesh current
Steps:
  KVL for each mesh
    Represent the voltage of the elements by mesh current
With controlled sources
  Represent the current or voltage of the controlled sources by mesh currents

## Slide 11: Mesh Analysis with Controlled Sources
Current controlled
Easy to represent control variable ix by mesh currents

## Slide 12: Mesh Analysis with Controlled Sources
Voltage controlled
In most cases, we can represent the control variable vx by mesh currents (refer to slides of Lecture 3)
Except that when vx is the voltage of current sources

## Slide 13: 台大碩士入學 (2012) – CCVS, VCCS
Mesh 1:
Mesh 2:
+
-
+
-
+
-
Notes: How about node analysis?

## Slide 14: Outline
Controlled sources
  Chapter 2.3, 3.2
Node analysis with Controlled sources
  Chapter 4.3
Mesh analysis with Controlled sources
  Chapter 4.3
Superposition with Controlled sources
  Chapter 2.4

## Slide 15: Superposition Principle
Example 2.10
  Find i1
We can find i1-1, i1-2, i1-3 separately.
set x2=0 and x3=0
set x1=0 and x3=0
set x1=0 and x2=0
find
find
find

## Slide 16: Superposition Principle with controlled variable
Example 2.11
  Find i1
+
-
+
-
+
-

## Slide 17: Superposition Principle with controlled variable
Example 2.11
  Find i1
set x2=0
set x1=0
The current through 2Ω is i1-1.
The current through 2Ω is i1-2.
Do not “turn off” controlled sources

## Slide 18: Superposition Principle with controlled variable
Example 2.11
  Find i1
set x2=0
Open circuit
+
-
+
-
+
-
KVL for the big loop:

## Slide 19: Superposition Principle with controlled variable
Example 2.11
  Find i1
set x1=0
short circuit
+
-
+
-
+
-
KVL for the big loop:

## Slide 20: Superposition Principle with controlled variable
Example 2.11
  Find i1
set x2=0
set x1=0
The current through 2Ω is i1-1.
The current through 2Ω is i1-2.

## Slide 21: Superposition Principle with controlled variable
Example 2.11
  Find i1
Can we use superposition in this way?

## Slide 22: Homework
Node analysis with Controlled sources
  4.56

## Slide 23: Homework
Mesh analysis with Controlled sources
  4.50
  4.51

## Slide 24: Homework
Superposition with Controlled sources

## Slide 25: Thank you!

## Slide 26: Answer
Node analysis with Controlled sources
  4.56: v1=8V, v2=8V

## Slide 27: Answer
Mesh analysis with Controlled sources
  4.50: i1=-2mA, i2=0
  4.51: (a) i1=0, i2=-3 (b) v1=12, v2=60, Req=infinity

## Slide 28: Answer
Superposition with Controlled sources